## Slide 1
PROJECT 6: Multi-Objective Bayesian Optimization
for Transparent Electromagnetic Interference Shielding
with Thin-Film Structures
Jungtaek Kim (Team Leader), Mingxuan Li,
Oliver Hinder, and Paul W. Leu
Two-layer system
Four-layer system
Six-layer system
Eight-layer system
Electromagnetic Interference Shielding
Protect a device from radio-frequency interference.
Transparency is required for specific applications such as spacecraft windows.
Multi-Objective Bayesian Optimization
Since two objectives are black-box, multi-objective Bayesian optimization is employed.
Random scalarization for both acquisition functions are used for multi-objective Bayesian optimization.
Problem Formulation
Simple thin-film structures are used for electromagnetic interference shielding.
Transmittance and shielding effectiveness are considered as objectives being optimized.
Material and thickness for each layer is selected by Bayesian optimization.
Search Space
Material choices
  Ag, Al, Al2O3, Cr, Ni, Pd, Si3N4, SiO2, Ti, TiN, TiO2, W
Thickness range
  [5, 20] nm
Bayesian Optimization
Gaussian processes with the Matérn 5/2 kernel
Expected improvement