## Slide 1: PROJECT 6: Multi-Objective Bayesian Optimization for Transparent Electromagnetic Interference Shielding with Thin-Film Structures
Jungtaek Kim (Team Leader),
Mingxuan Li, Oliver Hinder, and Paul W. Leu
Notes: Hello, everyone.
Today we are talking about our hackathon project, multi-objective Bayesian optimization for transparent electromagnetic interference shielding with thin-film structures.

## Slide 2: Electromagnetic Interference Shielding
Protect a device from radio-frequency interference.
Transparency is required for specific applications such as spacecraft windows.
Notes: Electromagnetic interference shielding is to protect a device from radio-frequency interference.
In addition, transparency is required for specific applications such as spacecraft windows.

## Slide 3: Problem Formulation
Simple thin-film structures are used for electromagnetic interference shielding.
Transmittance and shielding effectiveness are considered as objectives being optimized.
Material and thickness for each layer is selected by Bayesian optimization.
Notes: In this project, we are interested in simple thin-film structures for electromagnetic interference shielding.
For objectives, transmittance and shielding effectiveness are used.
Our goal is to maximize both objectives by selecting material and thickness for each layer.

## Slide 4: Multi-Objective Bayesian Optimization
Since two objectives are black-box, multi-objective Bayesian optimization is employed.
Random scalarization for both acquisition functions are used for multi-objective Bayesian optimization.
Notes: We maximize two objectives regarding transmittance and shielding effectiveness using multi-objective Bayesian optimization.
To implement the multi-objective Bayesian optimization, we use random scalarization for both acquisition function.

## Slide 5: Search Space
Material choices
  Ag, Al, Al2O3, Cr, Ni, Pd, Si3N4, SiO2, Ti, TiN, TiO2, W
Thickness range
  [5, 20] nm
Notes: Our search space contains twelve material choices and a thickness range from 5 to 20 nanometers.

## Slide 6: Bayesian Optimization Setting
Gaussian processes with the Matérn 5/2 kernel
Expected improvement
Notes: For the Bayesian optimization, Gaussian process regression and expected improvement are used.

## Slide 7: Experimental Results
Two-layer system
Four-layer system
Six-layer system
Eight-layer system
Notes: We present experimental results in this page.
Multi-objective Bayesian optimization is quite effective for finding the Pareto frontier of two objectives as shown in figures.

## Slide 8: Thank you!
Notes: Thank you.